Shire of Dumbleyung

Tender NEW – Stubbs Park Changerooms

ADDITIONAL Construction Specifications

NOVEMber 2020

DEMOLITION AND ASBESTOS REMOVAL

- All asbestos on the sides of the existing stadium (grandstand) is to be removed and reclad to match the new changeroom. This includes the sides of the ‘existing stadium structure over’ shown on Elevation 1 on Sheet 5 and Elevation 3 on Sheet 6 (will require elevated work platform).

- All wall framing and cladding in the changerooms (including the walls adjoining the storerooms) are to be removed.

STORMWATER

- Stormwater shall be disposed of in a manner which minimises the potential for erosion damage such as soak wells or drains to existing pits.

WINDOWS, DOORS & GLAZING

Windows

- Aluminium frame with powder coat finish.  Windows are to be horizontal sliding sashes with keyed lock bolts enabling sash to be locked in closed position or with a 100mm opening.

- Window lock keys keyed alike on all opening windows

- All windows are to have insect screens.

- Glazing to wet areas to be obscure. All other windows to be clear.

Door Frames

- Externally: Steel frames to suit 920mm wide doors.

- Internally: Steel frames to suit 920mm wide doors.

Doors Generally

- All external doors: Water Resistant 920mm minimum width external steel hinged flush solid core timber door with three 100mm fixed pin broad butt hinges, opening outwards.

- All externally doors (except the storeroom door) to have self closers installed.

- Wet Areas: 920mm width hinged flush timber door.

- Wet area partition doors to have privacy locks with inside turn snib and emergency keyway for quick entry by screwdriver or similar.

- Other flush timber doors: cellular core and pre-painted white hardboard facings, 920mm clear opening and steel hinged.

- Internal doors to have latch sets (keyed alike).

Keying

- Door locks in each changeroom shall be keyed alike.

- Outside storeroom door to be keyed separately.

- Supply two (2) full, complete sets of keys for each door.

Door Seals

- Provide an approved grooved aluminium and rubber door seal to each external hinged door.

OTHER GENERAL REQUIREMENTS

Construction

- New structure is to be steel framed (including internal wall framing) and externally clad with colorbond.

Insulation

- Provide R1.5 wall insulation (where required) between studs on external frames and to internal walls with R2.5 minimum ceiling insulation winter thermal resistance insulation on top of ceilings – not to be loose fill.

- Provide grade A reflective foil laminate as basic quality sarking under metal roof sheeting and to external face of studwork.

PLUMBING

- All plumbing works to comply with the Plumbing Code of Australia and AS 3500.

- All water and sewerage connections are to be made to the existing services.

- All toilet fixtures, etc to be caroma or equivalent standard.

- Provide one external tap outside the “away” changeroom.

- Sinks in wet areas mounted in laminate vanity cabinetry.

Showers

- Supply and fit a combined concealed assembly with mixer stop cocks and a 150mm long x 45mm diameter adjustable arm fixed 1800mm above floor of shower recess with a 100mm swivel anti-splash shower rose.

- Stop cocks to be offset to the shower rose.

Water Heating

- Supply and fit continuous flow gas hot water systems to handle each changeroom (3 showers, 2 toilets and 1 vanity basin), the umpires room (disabled toilet, shower & vanity basin) and the medical room (vanity basin).

ELECTRICAL

- All electrical works to comply with the National Construction Code and relevant Australian Standards.

- All cnnections to be made to the existing electrical supply.

Lighting

- Internal lights to be LED and suitable for grid ceiling with protection from ball damage in changerooms.

Exhaust Fans

- A minimum of 3 exhaust fans in each changeroom to be on the external north wall.

- Exhaust fan to be supplied to umpires room (flued either through the roof or the wall).

External Areas

- Light fittings: Vandal resistant and weatherproof LED lighting is to be fitted over all external doors.

OTHER MISCELLANEOUS ITEMS

Ablution Partitioning

- Supply and fit pedestal mounted laminate partitioning for each toilet including door and lockable hardware.

- Supply and fit pedestal mounted laminate partitioning for each shower including door, with dividing panel protecting bench space, and lockable hardware.

FINISHES

Internal Wall & Ceiling Finishes

- All internal walls shall be water resistant “Villa Board” and flush jointed (except where tiled) and shall have a smooth, even surface for painting.

- All internal ceilings shall be grid and white laminate tile (suitable for wet area).

- Supply and fit ceramic tiles on walls as per details shown on working drawings.

- Cut edges of wall tiles shall not be left exposed.

Internal Floor Finishes

- Wet Areas: Supply and fit ceramic floor tiles with approved non-slip surface.

- General Floor: Concrete with a non-slip finish.

- Cover junctions of different interior floor finishes with protective capping / diminishing strip fixed to floor.

EXTRAS (TO BE QUOTED SEPERATELY)

Painting

- Paint all exposed surfaces of the works other than colour finished metal other than primed roof plumbing, roof sheeting, roof tiles, face masonry, concrete, glazed, gloss, plastic, vinyl, aluminium, stainless steel, chromium plating or melamine surfaced particle board.

Additional Bench Seating

- Provide bench seating and clothes hooks to each changeroom (on the eastern, south eastern, south western and western walls of the changerooms.

Urinal

- Provide a urinal in each of the changerooms (additional to the existing two toilets).